Timescale for mass transfer:
Should be the same as fluid because particle convection is dominant.
Check if dominant:

Check BC of particle

01: contact line not pinning, start from 90 degrees.
diverge, error1&error2 show NaN

02: check if error1&error2 calculated right with error1p, error2p.
still NaN

03: check which residual error gives NaN. use simple mesh.
si & cp on the free surface.? check sf&sj on free surface(KBC & accumulation)
jacobian rows of variable si&cp on the free surface also NaN
these all happened at the second step, which means the first step solves to strange values which exist only in the surface conditions.

check surface integrals within sf: NaN comes from flux. add a proof for flux: if r>1, report the error.

NaN can be checked by setting debug_NAN=.true.
change the code to write NaN information in a file "NaN_check", where to pause (in newton_raphson)

dynamics.dat from stepwise graph shows that the drop base extend while the height decrease. not know why this happened, because I predicted the drop to shrink with no base movement.

set u=v=0 to see results: NaN in solution. Jac does not have 0 or NaN rows, but solution goes to NaN. do not understand...

change back to no-simple-mesh, only use one thread, strange. change check_0_in_Jac back to 0, solves it.

real mesh, u=v=0: sol error NaN, Rsi NaN.
no u=v=0: fist step ok, then r>1.
realize that all these problems come from the divergent flux condition. set flux to be 1 always. solved it.

no u=v=0, flux=1: drop shape not well mantained. solution oafter first step: rmax=~1.8, mesh overlap

back to all normal conditions, fix contact line, only set cp not to change: converge well.

cancel fixed cp: converge well. so the problem before intern was only with mass conservation. killed.

04 not pinned contact line: diverge. if set cp=0, still diverge. if T=cp=0: still diverge. u=v=0: diverge

05 very large diffusion: Pep=0.00001. killed

06 Pep=0.01, initial theta=50. finished.

07 with T change. did not change back to divergent flux(04,05,06,07). particle concentration behave well. killed.

08 divergent flux: particle concentration still behave well. killed.

09 with substrate: behave well. dt always the smallest. change to a large smallest dt(10t)(5e-6). finished.

10 large dtmin=1e-5: answer same as 09. killed

11 dtmin=1e-4: stopped somehow

12 restart 11, stopped at timestep12, because more than 11 steps are needed to converge, but still quadratic converge, so it is fine. need to change the maximum steps allowed if using dtmin=1e-4.

13 check if dcp influence dt. 13_1 solve with cp, 13_2 set cp not to change with BC.
(do not include dcp when calculating truncate error, so that dt is predicted the same as before.)

found that the element number is not the same as before(when cp is not added).

14 change the element numbers to the same as before.
found that the angle_c_degree is negative for the first mesh change. so added a line in var_cal for angle calculation: for the first time mesh is adjusted, do not calculate angle_c. fixed the bug.

notice that even without solving cp, trunerr still not the same. too large for the new code. use git diff, found that trunerr calculation method changed. change back. now dt is the same.

solved dt-too-small problem. upload to git!

15 no Maran. see if cp is different.

16: try to figure out the mass conservation failure. particle mass exceeds volume*cpmax, so cpintfac is wrong. figured out and fixed the problem: rintfac, cpintfac, etc need to be set 0 within (k,l) loop. this is why cp mass not conserved, and also why drop volume was 26 instead of less than 1. fixed.

It seems that the Marangoni flow does not have much influence on particel concentration. is Ma very small near the end? If so, concentration is capillary affected.
17: increase beta to see under what condition does Marangoni flow affect particle concentration. in "parameter", insert "beta0=1000*beta0"
this lead to sharp jump in the first timestep, may need to damp soln in the first timestep.may need to increase beta little by little.??? not finished. worry about later.

found that the Pep was set to be very small because of previous debugging process. That is why no difference shows: particle diffuse uniformly instead of affected by flow profile/convection.

results with maximum packing, but wrong BC for packing

pack_condition=NaN was cause by 2^1111, too large

18: dtmin=1e-6, no Marangoni. killed.

19: dtmin=5e-5, no Marangoni. ran 13h.
20: no include cp when calculating trunerr, no Marangoni
21: Marangoni

results with no packing
22: no Marangoni. (not converge at timestep2)resolved: due to BC change but split_sol didn't change.
Dp=Dp*10, 1um particles.(results in timestep1 presents large cp at the top of the drop, which is wrong, should be the contact line area.)
mainly accumulate at the contact line.accumulcate alittle at the top, and this affect is more obvious in the very initial stage, and much less later because corner accumulcation is too dominant.

23: 100nm particles, no Marangoni. accumulation at the top is too much, always dominant. cp values at the surface and the contact line is ridiculously large

24: Marangoni, 100nm. lost stability, cp chaos.
[idea]: make temperature and streamlines stable first, set up the stable circulation first; then add partile. this may avoid the chaos due to multicirculation at the initial instable stage.worked!
25: Marangoni with 1um particles. behaved well except it stopped due to full max packing
25_1: no packing stop condition. stopped due to "bus error core dumped", not sure what it is, but may be related to being run with elastic. rerun with thunder.???

26: from 90 degree. stopped due to the "cp no change anymore" condition. behaved well before that.
26_1: run with no cp stop condition. goes to wrong solutions. cp can not be lower than -1. so need to decrease dt by incorporating cp in trun_err.???

27: use [idea]. stopped due to "cp no change anymore". need to rerun
found that fixed cp BC was not correctly set up before: need to judge if the element is in drop phase first, or Ncp points to other variables maybe for other nodes.

27_1: 100nm particles. numerical instability happened soon. consider putting cp into trun_err.

28: include stagnation location. 1um particle, Marangoni. draw surface cp. numerical instability happened early. graph every step to see?
29: 100nm, include cp trun_err. instability angle=49.771, this is around the time when dt reaches 1e-6.
30: 1um, start from 90. instable from the very first timestep for cp.

31: no substrate. need to comment out size_change_3. not using the initial cp fixed BC. instable right from the start.

32: no substrate 50 degrees. initial mesh change back to size_3. cp<-1 from the very start.

33: dimensionless cp change back to cp/cp0 instead of (cp-cp0)/cp0. cp<0 from the very start.

34: cp l2error, not divided by max value. did not converge. timestep=1, cp goes more and more negative by step. may need smaller initial dt.

35: smaller initial dt 1e-6. still unstable.

cp change after flow stable, but changed the stability criteria. initial dt back to 1e-5. graph everystep to see, graph_mode change to 1 after stability is setup. graph subroutine is wrong, when graph_mode change to 1, not restart writing dynamics.dat

36 change graph subroutine to solve the above problem. graph subroutine is good now.
but, dt when cp starts to be solved is too large may be the reason to cause instabality. set back to 1e-6 when starting to solve cp.

37: dt is set back to 1e-6 when starting to solve cp, and treat as just start calculating in prediction subroutine. not converge

38: dt=1e-7. need smaller dt

39: dt=1e-8. need smaller dt

40: dt=1e-9, graph_mode always 0. dt is still too big

------------------used wrong Pe: too large, it is for 100um particles---------

41: dt=1e-5, start cp right away(init_stability=1), Dp=1nm. behave well. killed
41_1: not include cp in trunerr. still need to analyze the resultsbehave well. maybe compare with 41_2 on the surface cp to see how much difference are there.

41_2: dt=1e-5, start cp right away(init_stability=1), Dp=1nm. behaved well till 5.236, dt not always small, as large as 1e-4 when angle (16,47).

42: Dp=10nm. may be unstable, cp lower than 0.99 emerged at angle=49.921. killed

43: Dp=100nm. unstable because dtmin is still too big for 100nm particles. killed.

44: no Marangoni, trunerr not include cp, 100nm particle. behaved well except cp at the surface and the contact line is too high, not physical.

45: no Marangoni, trunerr include cp, 1nm. Got results

46: Marangoni, 100nm, trunerr include cp, start cp after profile stable.? start cp with FTS of 1e-5 is too large, diverge. next, try a smaller FTS.
46_2: FTS 1e-7. still diverge.

---------------------------use no substrate to get quicker results-------------

47: Marangoni, 1nm, add substrate, trunerr include cp, start cp after profile stable. did not converge once cp was solved. If this even failed, the problem with 46 may not be dtmin. Need to figure out why this failed. May help with 46.

48: Marangoni with substrate, 1nm, start cp right away(this is done by setting init_stability to 1 in initialization). Got results.

49: more elements for 10nm, no substrate, dtmin=1e-8. As low as dt=6e-7, very slow. Killed at angle 49.81. should be the same as 51(same condition except mesh).

50: no Marangoni, 10nm. Stopped at angle 7.5.

51: 10nm, Marangoni, no substrate, NEL=15; try with fsize change to make elements more concentrated to the free surface, see if dt decrease; also, plot normalized cp_surface. [1] solved overnight(more than 12h), converge still at angle 6.15.

52: 10nm, Marangoni, substrate, NEL backto 8, make mesh accumulate to free surface more. dt is even bigger than 51, so do not need 51 any more: dt small, each step takes twice solving time, so too slow. converged till angle 6.004. at first when stability was not reached, cp<0.99 also happened.

53: same with 52 except 100nm. diverged at angle 48.98.

Oh my god! I've been calculating with uniform flux all the time!!! Need to rerun everything. This may help with convergence: with uniflux, cp at the surface is too high (the surface where r=0 is even more higher), can cause divergence; with physical flux, cp is high at the CL, this also happened for no_Maran, so may not be a problem. I saw that there was no capillary-induced stagnation point in 52, so found out.

54: normal conditions with 100nm. totally diverged.

55: 100nm, no Marangoni. stopped at angle 43.38, cp at CL&surface got too high, especially at CL: 6e4. Cp=130 emerged first at angle 49.1.

56: 10nm, no Maran. Tells us when maximum packing is reached. Cp=130 emerged first at angle 37.

57: 10nm, Marangoni. stopped at angle 13 due to precision (diverge and then converge when repeating for many times, so I want to change the flag.)

58: 1nm, no Maran. Converged till angle 6.5.

59: 1nm, Marangoni, substrate. killed. See 59_2
59_2: 1nm, Marangoni, substrate. got results. Stopped at angle 7.8 because ”too many files open”, so it could have been continuing.

change graph to plot cp_normalized. run to check. Work well.

60: 100nm, Marangoni, NEL15, no substrate. stopped because of “too many files open”(code error). Still need to organize the dynamics.dat to see what happened before stop.

some simulation diverge and then converge.
change diverge flag so that if the repeated timestep converges, continue to next timestep.

Rerun 1nm, 10nm, M, nM

61: 1nm, no Maran.[1]

62: 10nm, noMaran. [4]

63: 1nm, Maran. [2] found that a timestep diverge and then converge when recalculating. I let the program to go to the next timestep if this happens. But the program paused because: during recalculation, graph every step, this setting lead to pause. Need to go back to the mode of not plotting for every timestep.

64: 10nm, Maran. [3]

if 100nm wont work, increase the humidity to reduce evaporation speed.

then compare if the time to reach maximum packing is postponed with Marangoni

65: 10nm, no Maran, radial_cp_accumulation, start cal from angle 33
65_1: restart without pause after radial_acc_cal. Calculated to less than 9 angle.
65_2: more precision near the CL for radial_acc_cal. Paused because si<-0.1. no useful data.
65_3: still carry on if si,eta is out of (0,1) range. Stopped because near the CL, z_surf is greater than the element domain boundary.
65_4: use cp_lower*dz to represent accumulation near the CL. [2]

66: 10nm, Maran, radial_cp_accumulation, start cal from angle 16
66_1: more precision. Start cal from angle 33. [1]

Till now:
Marangoni or not; particle needs to be smaller than 100nm: 10nm & 1nm work; radial distribution can be calculated, and the calculation can start from a certain angle.

To facilitate future debugging & comparison, make code work without solving T.
no_Maran=1 means no Marangoni stress. Under this condition, T does not need solving.

Next: all sentences containing NT needs changing.

67: solve with no T variable. The code to solve with no T works! But there seems to be problem about the trun_err, because the timestep is always small, not consistent with the previous calculated value.
67_1: change prediction subroutine to include no_Maran condition for NTs as well. Worked. BTW, changed other subroutines containing NTs.

68: Resisp.
sol_error of cp for node 1&4 does not converge, which means the equations at close packing is not accurate. So this comes from Resisp. Use smoother function.
68_1: smoother function leads to quadratcia convergence. But mass is not conserved. So need to change the equations.

69: update equations to include grad(R).
surface dRmi/drj is it because VI not excluded? Or just SI is not correctly defined? Rsi_SI (KBC) was not even correctly defined: flux is also a function of r. Need to check if this has effects on stagnation location results!!!

confirm the results of jacobian_check.
go back to no-Resisp version, see the results of jacobian_check.
Same: with no_Resisp, d(Rm_VI)i/drj & d(Rm_VI)i/dzj still shows error when TOL is as small as 1e-7

70: use Resisp for convective terms, not for diffusion terms. Converged. Used Resisp = 1
Particle mass increase.(but not big, increase speed is the same as before 65_4)
70_1: smooth Resisp: steepness 8e1, drop_location 0.999. mass loss. Results similar to 70_2
70_2: real Resisp: steepness 8e3 1e3 5e2 not converging; 1e2 converges. Mass loss when maximum packing reaches.
(70_3: check again smooth Resisp: steepness 8e1, drop_location 0.998. since 1e2 works, do not need to check, stopped the sim.)
(70_3: steepness 2e2: not converge at step 78.)
70_4: when above cp_pack, Resisp behaves the same as cp_pack. Diverge at step 19. this Resisp does not work. Revert back to the original Resisp.

Realized that the mass conservation is due to wrong BC. Resisp cannot be applied to the whole Jevap term.

71: smooth Resisp with Marangoni. Stopped at angle 38.89. particle mass behavior is the same as 66_1 before divergence: maximum packing effect very small yet.
CL node cp 2.02. the divergence may be related to cp exceed cp_pack. So when above cp_pack, Resisp behaves the same as cp_pack
71_1: Resisp no change above cp_pack. Stopeed at angle 40.2

72: changed BC of Rm. Mass is conserved. 0.125-0.123.

73: Marangoni on: stopped converging at angle 37.46.

74: Marangoni off, cp_pack=20: stopped converging at angle 33.48.
75: cp_pack=100: stopped converging at angle 36.

------------------------------------not doing Ressisp, but to fix by element--------------------------------
76: check if revert successfully back to before Resisp: good
76_1: check with Marangoni: good.

data file particle mass, write angle_c in degrees.

77: macimum packing fix element-wise. dt too small 10e-8
77_1: minimum dt 1e-6. Stopped because 77_2 seemed fine.
77_2: minimum dt 1e-5. Stopped to recalculate from Thunder. Did not save all data due to insufficient space. See 78. it seemed that the nodes still move with maximum packing???
78: same with 77_2, do not graph every timestep, graph every 50 steps. velocity profile was affected near the packing. Packing behavior was not physical. Diverged at angle 48.2.
78_1: 1e-6, graph every 500 steps. Stopped due to insufficient space. velocity profile was affected.

79: only fix cp at the packing region.
The cp in the packin gboundary node increase very slowly. I think it's because the boundary node cp is fixed and cannot go up, which is the loss of mass since accumulation happens on the node.

Lc changed to 2e-3

80: not fix boundary nodes. BcpackingE&N need to be initialized to 0 for every timestep, didn't do before![1] particle increases.
81: not fix cp for any node in split_sol.[2]

noticed that cp change a lot in the packing region. Need to make sure if dcp=0 is imposed or not. It was imposed. The problem is that if we assume the surface not fixed, then accumulation due to surface moving still increase cp.
No cp of node 9 decreased.

Corrected JacWhole a little bit during debugging.

Why was cp, r, z not fixed in the packing region?!!!

81: check if check NaN is correct: Newton_interation, if error NaN, check_0=1. check what happens if I fix cp for certain nodes after timestep 5.

cp can be fixed
from the very start with uniform intiial values or gradience
for the first 1000 nodes, but then go to NaN after a while.
NaN if start from gradience 1+r, and only fix parts
but work if start from 1-r, only fix parts, give NaN at timestep 41.
81_1: fix first 1000 nodes after 5 timesteps, initial cp=1
81_2: fix first 10000 nodes after 5 timesteps, initial cp=1-r

So we cannot just give random conditions and fix arbitrary nodes.

I think we still need to fix the cps in split_sol. Just do not use cp_pack, use their last value. When using cp_pack, we are increasing the cp values, thus resulting in mass increase.!!!

It may also be related to prediction. If predicted sol is far away from 0, we may end up going to the wrong solution. → If packing is imposed in split_sol, then solpred was set to cp_pack, because split_sol was executed right after solpred defining.
split_sol was executed for prediction, after every newton iteration, at the end of this timestep.
Previously, dt was very small because trunerr was large, which came from the wrong solpred of packing. So do not include packing part into trunerr calculation.

81: packing 1.3, see if packing strategy is better: if particle mass is conserved. Yes.
81_0: packing 2.0. see.
81_0_1: updated trunerr calculation. See if dt was increased. Increase a little bit, not much difference, so killed. See dt comparison in folder 81_0 as the graph.

82: cp_pack=30. Fix in split_sol. [3] particle increases a lot after packing.

82_1: same condition, improved cp_packing strategy.[2] particle decreases a lot... I think this may be cause by not fixing radial accumulation.
Check: set a bantoumo boundary and see how accumulation on the bantoumo acts. The bantoumo is on a certain column#. Or from 64+16*n+1 to 64+16*(n+1) elements, the left side. Comment out packing condition to do this.

I just realized that I was not supposed to fix cp in the packin gregion. That will only cause mass loss in that region, because of the disfunction of surface accumulation.
(But this is nort sufficient to account for the large mass loss and the fact that the packing regin won't grow fast.)
I should just set a boundary saying particles do not come across. And then let the particles do their own business on each side of the wall. So let's first set a fixed wall, and if that worked, we'll later use the moving wall based on the packing (need to change var_cal, split_sol, BC).

From now on: doing the semipermeable case!

Only did BC from the left side. --> in packing, only do from left side too.
Found a debugging sentence at the end of si_SI. Need to delete when going back to packing project.
Packing region BC & splits_sol need to add if(s_mode.eq.0).

84: semipermeable project. [1]

Still need to debug. Not converging. See terminal for jacobian_check results. Errors for all BcwallE. This came from sideN not assigned. Use sideN=1 is OK.

Put semipermeable wall before or after free surface particle accumulation seem no difference for secand method, not sure if they are different for results or particle mass.

84_1: wall BC with vs(node moving). [1 ]
84_2: wall BC before accumulation BC. [2]
84_3: wall BC together with accumulation [3] NaN happened. Need to check why. Changed to simple mesh. Simple mesh gives no NaN. Need to figure out why.

85: packing project, see if m2=particle_left+particle_packing is conserved. No.

83: fix r&z as well, cp_pack=2
dt was too small, came from u&v, because at packing region, flow profile was wrecked.
How to fix: do not fix r&z, still solve flow as before, but store particle radial mass in the packing region to preserve mass.

In the future, for preciseness, may need to change Rm on the surface to u,v determined instead of J, because if packing happen on the surface, SI need to be added both by packing & accumulation, viz. VI + SIpacking + Siaccum.

I found the definition of Jp_r_right is problematic in values_in_sj. Also, the application of Rt_SI & Rm_SI on the CL node is problematic.!??????!

maximum packing condition: the particle mass was not conserved.need to change BC for maximum packing boundary.not done???

86: check if master works. Yas!

87: set Ma number. Split no_Maran into Maran_flow & solve_T. Results same as 86.

88: use Ma number: MaN.
88_1: first check fixed_Ma=0
88_2: then fixed_Ma=1 [3] multi-circulation at r=0.92, but seem to be fading away. [results!]
1)before angle=45.5 flow was not stable, before angle=44.9 cp was not stable. In the future, we may consider only plot angle<40 in dynamics.dat, put early results into chaos.dat.
2)From total mass, after angle 18 mass loss was serious: 10% at last. It should be caused by ridiculously high cp value at CL, which prevents valid calculation of total mass (single node high concentration cannot be put into integration correctly).
1. Therefore, accumulation boundary may still be needed.
2. Adsorption to surface concentration may help with the mass loss.
3)We can still get a lot of informaiton between angle 20-40. just plot more timsteps between this range as described in 1).
I plotted dt~angle. Between 20-40, dt was large, so we can graph every timestep.

88_3: use a opposite sign of MaN: still multi-circulation at r=0.92. Found out that that was initial instability. After angle=49, timestep was larger, and multi-circulation faded away. Single circulation after angle=43. a problem with radial_accum?
88_4: check the problem with radial_accum: This was because z_surf was not correctly given.!
88_5: check to see if I can ignore the transient terms: results same, still has multi-circulation at the start.
88_6: set trans=0 & inertia=0: still initial multi-circulation.

89: give the option of solving cp or not.
89_1: solve_cp=1 compare with 88_6 to see if exactly the same. Yas!
89_2: solve_cp=0. It finished real fast!
89_3: write psol in dynamics.dat

Is init_stability used for cp??

trans=0
90: change KBC for trans=0 !!
90_1: change too fast, ridiculous results. Huge v magnitude. Domain flipped with elements out ot domain.
90_2: turn off Marangoni. Still not a good initial guess.
Try to first solve trans and then change to trans=0 after good guess? Maybe will work, but not worth it.
Gradually increase evaporation J0 & Marangoni Ma may work. but not worth the time to do.

I can run 2 simulations: 1 full 2 no inertia. Compare stagnation point locations to see their influences.
91_1: no inertia.
91_2: no inertia, tailored stagnation data file. Did not tailor well, need to add tan(angle). Finished.
91_3: full NS.

run simulations with changed substrate dimensions
92_1: l_s=2.0
92_2: l_s=4.0 plot ls_comparison: green ls=1.3, blue ls= 2.0, red ls=4.0. blue & red total overlap, green has a little shift (5um).
92_3: d=1.0
92_4: d=0.5 [1]
substrate dimension & element were changed!

The observed stagnation point could be the turning point . To find the location:
1. Precisely, du/dz=0
2. Simply for code, first try find du/deta=0 for region1 & du/dxi=0 for region3

93: check if turning points are found. Ma fixed negative. Yes, but with a little problem of r_change calculation. Fixed
93_1: Ma positive. No turning points after initial instability.
93_2: move stagnation&extremum to the module. Negative Ma. Stagnation plots well.
93_3: TP also exclude CL or initial instability.
93_4: eta1-eta2<0.5e-2.
93_5: update eta1 to move to eta3. Otherwise the middle value method is not accurate.
93_6: debug for TP calculation. It seems to work well. So the discontinuity may come from using dudxi to substitute dudz because xi changes by element.

Change Ma for reverse Marangoni.
94_1: Ma=100
94_2: Ma = 1000
94_3: Ma = 1e4
94_4: Ma = 10 [3]

95: fixed Ma working on cp. [2]

divide plots into dynamics.dat & initial_instability.dat
Then add adsorption equations. CL node has two surface concentrations, so that one is deposited, the other can diffuse on the surface.

96: substrate adsorption. Found negative substrate mass, realized the abs(rsi) is needed. Modify and rerun. Still negative substrate mass. Cp at r=z=0 increase crazily. There's something wrong.
96: Da = 100
96_1: set Da=0. Seems fine.
96_2: Da=1.0
96_3: Da = 1.0e5

97: with Marangoni flow. Fixed Ma (natural). Da=100?(maybe).
97_1: Da = 10, Ma = 10
97_2: Da = 10, Ma = -100

98: no fixed Ma.
98_1: Da=1.0. cp_average correction. Record Da_sub value, flags for adsp.
98_2: Da = 10.0 [1]

surface adsorption
99: Da_surf1=100, Da_surf2=1. Not converging after a few timesteps. Total mass not conserved.
99_1: fixed mistakes by sekand method. Mass conservation not achieved, negative gamma.
99_2: add dilatation term. Negative gamma.
99_3: only Rms1&2: negative gamma at CL, smaller mass loss. Cp goes to negative.
99_4: Rms1&2&32: sudden plump may be due to negative cp.
99_5: model modification: Da1*gamma*cp.
99_6: set Da1=Da2=0 to see if surface concentration conserved. Surface mass decrease a lot.
99_7: fix mistakes in Rms3 (missed a SQ**0.5 when deriving by hand). Surface mass increased.
99_8: angle 90, CL not fix, need to set base_mesh=0 for CL moving!!. This only checks dilatation.
Next commit “works for surf_adsp alone, still need to adjust for both adsp on”
99_8_1: 99_8 somehow has small velocity near CL, so set u=v=0(p=0 needs to be set together, otherwise does not work somehow.) gamma not changing, so dilatation not working! Dilatation is with normal projection of (rdot, vdot), not (u,v). They are different because of evaporation.
99_9: changed dilatation terms to be with (rdot, vdot), which is the surface velocity. Results?see tomorrow.
99_10: comment out Rms terms except Rms1&Rms5. Dilatation term is wrong.
99_11: new dilatation&stretching term Rms6. Worked.
99_12: back to CL pinning again. Gamma ridiculous, seems related stretching.
99_13: used 2H term for dilatation.
99_14: not pinning. Changed 2H term.
99_15: pinning.
99_16: no gamma diffusion.
99_17: no diffusion or convection, did not help. Trying to do 2H with 2sin(theta)/R, with no diffusion or convection or streching. As expected.
99_18: add convection and adsorption(Da=0). Roughly makes sense. mass_free increased a little, probably related to the loss of stretching term. Refer to 99_19. plotted the surface velocity.
99_19: add streching. The problem was with stretching. Used new terms for streching, rerun. Still prblem
99_20: set CL element to have no stretching term. No ridiculous seesaw, only four nodes has ridiculous value. I'm sure the error comes from the abrupt change of surface velocity. Put results in 99_19. then run new simulation.
Every term on.
99_21: turn on counterclockwise Marangoni, may help with CL stretching.
99_22: Ma on, no stretching.
99_23: Ma, not fixing Ma. To see stretching causing accumulation between two circulation.
99_24: fix Ma. New stretching. Did not work. Then use vs = v – Jn. Did not work. Used coarse mesh for quicker results. Observed that the wiggles happen at the stagnation point. Then decrease Ma=10, no wiggles.
99_25: Ma=10, original mesh.
99_26: Ma=100. Stopped at angle 48.4
99_27: no fixing Ma. Natural circulation.
99_28: Ma=-10. Initial gamma =0, Da=1
99_29: Ma = -100. lost precision for gamma at r=0, stop converging.
99_29_1: smaller Da. Helped. To angle 28.8.
99_29_2: include gamma into trunerr. Did not help.
99_30: no Maran. Natrual adsp (gamma0=0) works.

To figure out why addsing substrate does not work anymore.
1: the reason was: SQr2z2 cannot be used in outer surface (the end of the substrate) because it was not defined for that surface. Just changed the one SQr2z2 back to reta**2+zeta**2, then it worked!

figure out a method to observe the difference between plug flow and Marangoni flow results. Difficulties:
1. hard to find a same contact angle. therefore, a fixed dt is necessary. figure out appropriate fixed dt: observe the dt used in adaptive timestep method. find an average value for each simulation. make capillary simulation several times of Marangoni simulation.???
2. [finished] a value to quantatively compare particle distribution. surface concentration, S-L interface concentration, radial mass (how to calculate?)

If Re very small, no need to incorporate inertia.
include Ma in the parameter value. Gives the idea of real Re, which is origianl Re*Ma.